## Slide 1
AI-GUIDED BATTERY COATINGS
interphAIse
interphAIse / Results through 22 October 2026
01
Can an LLM choose
the next battery
coating to test?
Why the LLM matters
What it achieved, step by step
Davide Tisi and Adem R. N. Aouichaoui
Notes: Opening: interphAIse asks whether an AI language model can take on one part of scientific work: deciding which material deserves the next calculation. We will explain the battery problem, the decision loop, and three stages of evidence. Main talk: slides 1–16, approximately 15 minutes. Slides 17–22 are technical backup. Authors: Davide Tisi and Adem R. N. Aouichaoui. The LLM is Haiku 5.5. All outcomes are from the completed archived studies through 22 October 2026.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 2
THE IDEA
The problem: a protective layer inside a battery
The cathode stores lithium. The electrolyte lets lithium ions move.
interphAIse / Results through 22 October 2026
02
A useful coating must
Limit unwanted reactions
at both contacts.
Stay attached to the
neighboring materials.
Lithium ions must also pass
through. That was not tested.
Notes: A cathode is an electrode that stores lithium. The solid electrolyte carries lithium ions between electrodes. Where these materials touch, unwanted reactions and poor contact can be problems. The coating is a very thin protective layer between them, so it has two contacts to satisfy. The project tests chemical compatibility and simulated adhesion separately. The broad battery objective also requires lithium transport, synthesis and cycling, which were outside these tests. Image is an AI-generated conceptual illustration, not a simulation or an experimental image.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/README.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/nonexpert_assets/provenance.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 3
THE DECISION BEING TESTED
Why the LLM is central
LLM = large language model. Here, it chooses what to calculate next.
interphAIse / Results through 22 October 2026
03
01
Connect chemistry to a candidate
Choose a known material and explain why it might work.
02
Use the last result
Read what failed or nearly passed, then choose the next test.
03
Make a prediction that can fail
State an expected result before the physical calculation.
Researchers define the task. The LLM makes choices. The physics tools calculate the results.
Notes: The motivation is that a calculator can score a specified material but does not itself decide which chemical idea is worth pursuing. The LLM supplies that selection judgment and can express a hypothesis in words. This is why it is central to the experiment. Humans still define the candidate menu, scoring rule, budget and scientific interpretation. Deterministic code validates the choices and reveals numerical results. We measure the quality of the decisions, not whether the model internally reasons like a human. The LLM selects existing structure IDs, rather than inventing new compositions.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/DISCOVERY_REPORT.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 4
HOW IT WORKS
One decision loop, repeated after each result
interphAIse / Results through 22 October 2026
04
1
LLM: choose a material
Record the proposed coating and its chemical rationale.
2
Tool: test the material
Return a numerical result from the defined calculation.
3
LLM: interpret the feedback
Compare the result with the earlier expectation.
4
LLM: choose the next test
Continue until the evaluation budget is used.
Notes: Read these steps as a loop: the fourth step becomes the next first step. In the controlled search benchmark the numerical feedback is read from a precomputed thermodynamic table. The LLM cannot see the full answer table. In the later physical pilot, new interface calculations follow choices and numerical forecasts that have already been recorded. Keeping these two forms of testing distinct prevents a false claim that the cheap benchmark saved expensive compute.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/ENVIRONMENT_PROTOCOL.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 5
STEP 1 / CONTROLLED SELECTION
First test: can it find a coating that passes?
interphAIse / Results through 22 October 2026
05
Choose from a fixed menu of known materials.
A calculation scores unwanted chemical reactions.
A material passes only if it meets the preset limits.
10 tries
per search
30 searches
per strategy, with varied candidate order
“Success” means finding at least one passing material. It does not mean a working battery.
Notes: The original menu contains 50 structure IDs representing 43 formulas. Two structures pass. Each strategy receives ten charged evaluations, repeated 30 times. Unknown, duplicate and failed queries still consume budget. The pass rule combines a thermodynamic reaction penalty no greater than 0.050 eV per non-Li atom with a band-gap proxy for electronic insulation of at least 2 eV. Lower reaction penalty is better. The rule was frozen before decisive runs. It is a screening criterion, not a demonstration of useful battery performance.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/INTEGRATED_DISCOVERY_RESULTS.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/ENVIRONMENT_PROTOCOL.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 6
STEP 1 / COMPARISON
Five strategies make the comparison fair
The same menu, the same ten tries, and the same definition of success.
interphAIse / Results through 22 October 2026
06
Strategy used in the charts | How the next choice is made
Uses results | LLM sees the outcomes of its earlier choices
No results | LLM sees its choices, but not their outcomes
Mixed-up results | LLM sees outcomes reassigned between materials
One list | LLM chooses all ten materials before any result
Random | Software picks materials at random, without repeats
The first four use the same LLM. Random search provides a simple comparison.
Notes: The archived names are iterative, sequential, shuffled, upfront and random. The shorter labels used in the main talk explain what differs. No-results retains earlier choices and rationales. Mixed-up results tests whether correct attribution matters, although occasional correct assignments and contradictions with earlier rationales remain limitations. All LLM arms use Haiku 5.5, temperature 1.0. No single comparison proves an internal reasoning mechanism.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/ENVIRONMENT_PROTOCOL.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 7
STEP 1 / RESULT
Using results improved the first search test
Successful searches out of 30, using the original 50-structure menu.
interphAIse / Results through 22 October 2026
07
Chart: Successful searches / 30
| Uses results | No results | Mixed-up results | One list | Random
Successful searches | 19 | 4 | 6 | 4 | 10
Correct feedback helped: 19 successes, versus 4 without results and 6 with mixed-up results.
Notes: This combines 120 original runs with the matched 30-run shuffled follow-up. Counts are 19, 4, 6, 4 and 10. Do not add the earlier ten-run preview. Exact random expectation is 36.33%, compared with the observed random 10/30. Iterative versus shuffled paired exact McNemar p is about 0.0044, unadjusted. The evidence supports useful feedback in this task. A fluoride-first rule designed after seeing the table succeeds by query two, so this result does not establish superiority over every simpler policy. The original candidate pool overlaps the expanded pool.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/INTEGRATED_DISCOVERY_RESULTS.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 8
STEP 2 / A LARGER TEST
The benefit changed with the battery materials
141 structures, three electrolytes, 450 searches across all five strategies.
interphAIse / Results through 22 October 2026
08
Chart: Successful searches / 30
| Sulfide | Chloride | Oxide (LLZO)
Uses results | 20 | 30 | 12
No results | 2 | 30 | 0
Random | 8 | 29 | 24
Feedback helped
Almost all succeeded
Random did better
Notes: The electrolyte is the material carrying lithium ions. Changing it changes which coatings pass, even though the cathode remains LiCoO2 at 4 V. There are 4/141 passing structures in sulfide, 55/141 in chloride and 17/141 in LLZO. The chart shows three of the five strategies for clarity; all five counts and planned statistics are in backup slide 17. Sulfide counts are 20,2,6,0,8; chloride 30,30,30,30,29; LLZO 12,0,4,1,24, in iterative,sequential,shuffled,upfront,random order. Every run begins fresh: this is not learning transferred between environments. The expanded pool includes the original 50 structures. Do not pool those studies as independent replications.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/ENVIRONMENT_PROTOCOL.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 9
STEP 2 / WHAT THE LLM DID
A real example: refining a near miss
Three consecutive choices in one sulfide search. Lower reaction score is better.
interphAIse / Results through 22 October 2026
09
Try | Material chosen | Reaction score | What the test said
6 | Li₃AlF₆ | 0.160 | Does not pass
7 | LiMgAlF₆ | 0.057 | Close, but still above the limit
8 | LiCaAlF₆ | 0.048 | Passes the 0.050 limit
The LLM kept testing related chemistry after a promising near miss.
One illustrative search. Reaction scores are in eV per non-lithium atom.
Notes: This is sulfide seed 202. The trace was chosen in the earlier analysis using the lowest seed with a typical first-hit position, before reading the rationales. The model tried familiar oxides and LiF unsuccessfully, then explored mixed-cation fluorides. It interpreted the 0.057 result as a near miss and chose the Ca analogue. The values are recorded scores in eV per non-Li atom, rounded to three decimals. Its proposed chemical explanation is a hypothesis, not a verified reaction mechanism. The observed sequence makes the delegated judgment concrete without treating one attractive example as proof. Source archive: agent commit, data/experiments/environment_v1/lpscl/iterative_r202.json.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 10
STEP 2 / WHERE IT STRUGGLED
On the oxide, the LLM tried fewer chemical options
LLZO is the oxide electrolyte in the previous chart.
interphAIse / Results through 22 October 2026
10
33
different chemical formulas
tried by the LLM using results
95
different chemical formulas
tried by random search
10 of its 12 successful searches first passed on tries 8–10.
Across 300 choices per strategy. Broad exploration was more effective in this test.
Notes: Formula coverage is pooled across all 30 runs, ten picks per run, not a single search. Random has 24 successful runs and iterative 12. Iterative makes 29 acceptable picks, 28 in queries 6–10, with 26 picks from LiAlSiO4 polymorphs. Random makes 33 acceptable picks. These patterns describe late and concentrated selection, not the model’s private cognitive process. A later practical-chemistry audit flagged five of 17 acceptable structures; 18 of the 24 successful random runs also found an unflagged candidate. The main endpoint remains unchanged, and there is no evidence the LLM intentionally avoided flagged materials. Details are in backup slide 19.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/data/reviews/llzo_chemistry_audit_20261021.json
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 11
STEP 3 / PHYSICAL CALCULATIONS
Next test: predict how strongly the coating attaches
interphAIse / Results through 22 October 2026
11
One known reference
The LLM sees calculated results
for LiNbF₆, then chooses two
more coatings from a small menu.
A prediction before the test
For each choice, it predicts
adhesion at both contacts
before the new results exist.
Adhesion = energy needed to separate a contact in this model.
Higher values mean stronger attachment under the tested conditions.
PET-MAD simulates the atoms. These results have not been measured in a real battery.
Notes: PET-MAD is a machine-learned interatomic potential used to relax explicit atomic structures and compute energies. It is a separate model from the LLM. The physical pilot uses the sulfide stack. Reference LiNbF6 is evaluated first. Feasible alternatives are LiTaF6, LiCaAlF6 and LiF; LiF does not pass the frozen thermodynamic rule and was not physically evaluated. The known-material menu and construction rules constrain the choice. The adhesion quantity W_adh compares relaxed joined and separated surfaces under fixed protocol constraints, per interface area in J/m². It is not measured fracture toughness. Three registry positions per contact were tested for each new coating.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 12
STEP 3 / PREDICTION CHECKED
First choice: the forecast worked for LiTaF₆
Its idea: replace niobium (Nb) with chemically related tantalum (Ta).
interphAIse / Results through 22 October 2026
12
Contact with the coating | LLM forecast | Calculated adhesion
Cathode side | 3.2–3.9 | 3.339 (within range)
Electrolyte side | 1.4–1.9 | 1.577 (within range)
Both forecasts held. It also predicted the weaker contact correctly.
Units: J/m². Forecasts were recorded before the new calculations.
Notes: The LLM chose LiTaF6 using an Nb/Ta chemical analogy. Exact selected-primary values are 3.338748412819128 and 1.5773585444472311 J/m². Both fall inside the archived prospective ranges. The electrolyte contact is weaker, as forecast. This is one successful material-level analogy, not a calibrated error model. Ranges were stated by the model and are not statistical confidence intervals. Registry selection minimizes relaxed joined-interface energy, rather than choosing the largest adhesion value.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 13
STEP 3 / PREDICTION CHECKED
Second choice: the forecast failed for LiCaAlF₆
The LLM expected stronger attachment than the calculations found.
interphAIse / Results through 22 October 2026
13
Contact with the coating | LLM forecast | Calculated adhesion
Cathode side | 3.0–3.8 | 1.427 (below range)
Electrolyte side | 1.4–1.9 | 0.744 (below range)
Both forecasts missed. The LLM acknowledged the failure afterward.
Units: J/m². It still identified the electrolyte side as the weaker contact.
Notes: Exact selected-primary values are 1.426710445485596 and 0.7435735865694895 J/m². Both are below the previously recorded ranges. The model’s final assessment acknowledged the Ca–Al miss. Its choice order remained LiTaF6 then LiCaAlF6, the same as its initial shortlist; the second was the only remaining acceptable candidate in the feasible menu. The pilot therefore tests forecasts but cannot demonstrate adaptive-selection gain. The final summary also misread a weaker-contact field as a minimum over registries. The archived response is retained, with an explanatory correction in the review.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 14
STEP 3 / RESULT
What the physical calculations found
Adhesion in the tested structures. Higher values mean stronger attachment.
interphAIse / Results through 22 October 2026
14
Chart: Adhesion (J/m²)
| LiNbF₆ (reference) | LiTaF₆ (first choice) | LiCaAlF₆ (second choice)
Cathode side | 3.6171 | 3.3387 | 1.4267
Electrolyte side | 1.6334 | 1.5774 | 0.74357
Ca–Al attached less strongly. The small Nb–Ta gap does not establish a reliable winner.
Numerical sensitivity and charged model surfaces still limit the physical interpretation.
Notes: The electrolyte is the weaker contact for all three coatings. The Nb–Ta gap on that side is about 0.056 J/m². Changing the electrolyte bulk reference shifts their values by about 0.121 and 0.114 J/m², larger than the gap. These are construction sensitivities, not statistical error bars. Ca–Al shows much lower primary adhesion, but its electrolyte thickness and bulk-reference sensitivities remain unquantified. All contact models are formally polar, so numerical convergence does not remove the electrostatic limitation. The final values supersede earlier pilot values obtained with different constructions. Full W_adh/W_sep values appear in backup slide 20.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 15
THE ANSWER
What the LLM achieved
interphAIse / Results through 22 October 2026
15
01
Useful feedback improved some choices
Strong gains in the sulfide tests. The oxide result showed a limit.
02
It made chemical hypotheses testable
Two adhesion forecasts held and two failed, all recorded in advance.
03
It assessed results, but still needed review
Its order stayed the same. A human corrected one interpretation.
We tested a scientific decision process. A better battery coating has not yet been validated.
Notes: This is the central conclusion for a mixed audience. Feedback utility is conditional on the environment and the benchmark. Forecast checking is valuable because the calculation can contradict the model’s words. The physical pilot had two choices and no repeated expensive-search control, so it cannot prove general predictive reliability, compute savings or adaptive selection superiority. The model correctly identified the weaker contact twice but misunderstood the meaning of min_W_adh_J_m2 in the summary. Human interpretation and independent validation remain necessary.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 16
TOWARD USEFUL BATTERY COATINGS
What comes next
interphAIse / Results through 22 October 2026
16
1
Improve how the LLM explores
Test ways to avoid repeating a narrow set of chemical ideas.
2
Test choices over more physical calculations
Compare LLM-guided selection with simple rules and random choices.
3
Check the missing battery requirements
Test ion transport, practical preparation and experimental performance.
The contribution: a measured test of AI-guided scientific choices, including where they fail.
Notes: These are future research directions, not completed experiments. A new study should preregister an exploration mechanism and compare policies on independent expensive decisions. Physical models need additional validation, particularly polar-interface treatment and missing sensitivity checks. A functional coating also needs suitable transport, processability and cycling behavior. The current bounded pilot is complete and does not require new calculations to reproduce its existing outcomes. The integrated code and viewer have since been completed in the separate final-integration worktree; this deck does not merge branches.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 17
BACKUP / STATISTICAL EVIDENCE
All five strategies and the planned statistical tests
interphAIse / Results through 22 October 2026
17
Electrolyte | Uses results | No results | Mixed up | One list | Random
Sulfide | 20 | 2 | 6 | 0 | 8
Chloride | 30 | 30 | 30 | 30 | 29
Oxide (LLZO) | 12 | 0 | 4 | 1 | 24
Successful searches out of 30, after ten tries. Holm-adjusted paired tests:
Sulfide: versus no results p = 0.0000458, versus mixed-up p = 0.00244.
LLZO: versus no results p = 0.00244, versus mixed-up p = 0.172.
Chloride: p = 1 for both comparisons. Six planned tests in total.
Notes: Counts are the primary frozen endpoint from the 450-run environment study. Exact paired McNemar tests use display-order seeds 200–229 and Holm correction across all six planned comparisons. Three survive the 0.05 threshold. Random comparisons are descriptive relative to this preregistered family. Acceptable pool sizes are 4/141 sulfide, 55/141 chloride and 17/141 LLZO. The frozen objective uses P≤0.050 eV per non-Li atom, band gap≥2 eV and equilibrated contact endpoints. It does not predict finite-temperature behavior, ion transport, synthesis or battery cycling.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/ENVIRONMENT_PROTOCOL.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/presentations/source/results_synthesis_2026-10-22.json
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/RESULTS_SYNTHESIS_2026-10-22.md
Archived outcome commits: agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. Original benchmark source: 750b382844fd64aaa46f96ce96be1871e992c0f1.

## Slide 18
BACKUP / OBJECTIVE INTERPRETATION
Acceptability, optimum-finding and practicality differ
interphAIse / Results through 22 October 2026
18
Question | Measure | Observed limitation
Can the policy find a passing candidate? | Acceptance at P ≤ 0.050 | This is the primary reported result
Does it find the pool’s optimum? | Best-bin discovery / regret | Sulfide: iterative 6, random 5 LLZO: all LLMs 0, random 2 (of 30)
Is the actual coating useful? | Transport, processing, electrochemistry | Not established by this evaluator
Is the search saving compute? | Cost of avoided expensive evaluations | Cheap tables alone cannot show this
Acceptance cuts through a ranking bin. Near-threshold conclusions depend on the frozen definition.
Notes: Sources: frozen objective and environment analysis. Two acceptable structures in 50; 4/141 sulfide,55/141 chloride,17/141 LLZO. P cutoff0.050 crosses bin2 underwidth0.020. Best-bin success is a separate endpoint. Expanded sulfide iterative6 random5; LLZO allLLM0 random2. Missing/invalid/ineligible candidates cannot pass. Threshold not changed after outcomes.
Sources pinned for this synthesis: davide 750b382844fd64aaa46f96ce96be1871e992c0f1; agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. No new live LLM or MLIP calls. Figures use the archived outcomes, not a new experiment.

## Slide 19
BACKUP / POST-HOC CHEMISTRY REVIEW
The LLZO audit qualifies the criterion, not the score
interphAIse / Results through 22 October 2026
19
5 of 17 acceptable structures were flagged for practical review:
LiIO₃, LiClO₄ and Li₅IO₆.
Random’s 24 successful runs | Count
Also found an unflagged acceptable candidate | 18
Succeeded only through a flagged candidate | 6
This is a descriptive partition, not a rerun with a new endpoint. Primary result: 24 versus 12.
The model is not proven to be making a safety judgment. Finite-temperature and processing limits remain.
Notes: Source: data/reviews/llzo_chemistry_audit_20261021.json and SYNC_ADEM_10.md. LiIO3 and LiClO4 have supplier oxidizer classifications; Li5IO6 is a family-level review flag, not verified compound-specific GHS. Supplier links and original reference are preserved in the audit JSON. Evaluator does include O2 products, so do not claim it cannot form gas. No evidence that Haiku deliberately avoided these candidates. Frozen criterion unchanged.
Sources pinned for this synthesis: davide 750b382844fd64aaa46f96ce96be1871e992c0f1; agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. No new live LLM or MLIP calls. Figures use the archived outcomes, not a new experiment.

## Slide 20
BACKUP / FINAL PHYSICAL VALUES
Relaxed adhesion and rigid separation are different
interphAIse / Results through 22 October 2026
20
Coating | Cathode Wadh / Wsep | Electrolyte Wadh / Wsep | Atoms C / E
LiNbF₆ | 3.617 / 5.168 | 1.633 / 2.967 | 696 / 880
LiTaF₆ | 3.339 / 4.728 | 1.577 / 2.911 | 696 / 880
LiCaAlF₆ | 1.427 / 4.322 | 0.744 / 1.490 | 720 / 1212
Wadh: separated slabs are allowed to relax.
Wsep: fragments retain their joined-interface geometry.
J/m². Primary snapshots unchanged. Later robustness checks are a separate record.
Notes: Source: final index; Wadh = (relaxed constrained separated slab energies − relaxed joined interface energy)/area, same model and reference conventions. Wsep uses separated fragments frozen at the joined geometry. It is not an experimental fracture toughness. Large Wsep−Wadh indicates relaxation of freed surfaces within this protocol. Chosen registry minimizes joined energy, not max Wadh.
Sources pinned for this synthesis: davide 750b382844fd64aaa46f96ce96be1871e992c0f1; agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. No new live LLM or MLIP calls. Figures use the archived outcomes, not a new experiment.

## Slide 21
BACKUP / PHYSICAL REALIZATION
The structures and convergence evidence are archived
interphAIse / Results through 22 October 2026
21
Notes: Source image: data/petmad/niflheim_batch1/cathode_reg_third_third/inspection.png at davide750b382. Actual LiCoO2(001)|LiNbF6(001), 696 atoms, selected (1/3,1/3) registry. Force trace is maximum free-atom force; fixed atoms are excluded. Their residual force remains a limitation. Vacuum isolation reflects finite-range8Å model, not long-range polar convergence.
Sources pinned for this synthesis: davide 750b382844fd64aaa46f96ce96be1871e992c0f1; agent 800ba0378779ce7df9038bc4857719a29c2fe0a7; physics 1b76eeb0330ae1ddee3720d76145c2b308725245. No new live LLM or MLIP calls. Figures use the archived outcomes, not a new experiment.

## Slide 22
BACKUP / ACCOUNTING AND HANDOFF
Archived evidence and completed integration
interphAIse / Results through 22 October 2026
22
Evidence / cost | Verified record
Environment study | 450 runs, 2,800 API calls, about $3.63 at recorded list rates
Physical pilot LLM | 5 / 10 HTTP attempts, about $0.006 at recorded list rates
New PET-MAD jobs | 26 / 36, all converged, 6,632 runner calls + 52 single points
Compute time | 25.4 min runner time; 47.5 min summed Slurm elapsed Reused work, bulk preparation and queue time are separate
Integrated delivery | Reader fix, code integration and structure viewer completed on the separate final-integration branch
Frozen decisions, later robustness, source hashes and limitations remain independently inspectable.
Notes: Scientific accounting: environment study 450 runs and 2,800 API calls; physical pilot five HTTP attempts, 26 new jobs, 6,632 runner calls plus 52 rigid-fragment single points. Cost figures are recorded list-rate arithmetic, not current pricing or bills. Runner times and summed allocation times differ and exclude queue delay.
Current engineering checkpoint: work/final-integration-20261022 at 91afca5 includes both collaborators, the final-index reader correction and the generated viewer launch fix. The integrated tree previously passed 227 tests; the viewer fix passed 13 viewer tests. These are recorded prior checks, not tests rerun to produce this deck. Main/davide remain separate.
Sources:
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse/FINAL_PILOT_REVIEW.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse-integration/FINAL_INTEGRATION.md
/Users/davidetisi/Documents/Work/DTU/OSI_Hackathon/interphAIse-integration/REPORT.md